## Slide 1
MicroSD software image and other materials available from bbb.io/techlab
Get to the Cloud9 IDE
Served on port 3000
Windows: http://192.168.7.2:3000
Linux/Mac: http://192.168.6.2:3000
See bbb.io/start for instructions on using Etcher.io to write a microSD card
The BeagleBoard.org Foundation is a 501(c)(3) non-profit corporation existing to provide education in and collaboration around the design and use of open-source software and hardware in embedded computing.
Plug into the microUSB on PocketBeagle to provide power and a network connection. Look for the “heartbeat” pulse on the USR0 LED to know the board has Linux up-and-running.
PocketBeagle® TechLab Cape Hands-On Coding Workshop

## Slide 2
TechLab Pocket Cape
TechLab Wiring Summary
P2_33
P1_29
P1_19
iio:device0
R: P1_33
G: P2_1
B: P1_36
P2_30
I2C2 iio:device1
SPI1 CS1
leds/techlab::seg*
0
1
2
3
4
5
6
8
9
10
11
12
13
14
PocketBeagle® TechLab Cape Hands-On Coding Workshop
USB-to-Serial Micro B
PWM Controlled Tri-Color LED
Buzzer
SPI 2-Digit 7-Segment Displays
I2C Accelerometer
ADC Light Sensor
2 GPIO Push Buttons
Reset Button
USB Host A with power
mikroBus Header www.mikroe.com/click

## Slide 3
PocketBeagle Expansion Header Pin-out
Great getting started information is at beagleboard.org/pocket
PocketBeagle® is an ultra-tiny-yet-complete, low-cost, open-source USB-key-fob computer.
Processor System: Octavo Systems OSD3358-SM 21mm x 21mm system-in-package that includes 512MB DDR3 RAM, 1-GHz ARM Cortex-A8 CPU, 2x 200-MHz PRUs, ARM Cortex-M3, 3D accelerator, power/battery management and EEPROM
72 expansion pin headers with power and battery I/Os, high-speed USB, 8 analog inputs, 44 digital I/Os and numerous digital interface peripherals
microUSB host/client and microSD connectors
PocketBeagle® TechLab Cape Hands-On Coding Workshop
PocketBeagle®

## Slide 4
#!/usr/bin/env node
var b = require('bonescript');
var LED = 'USR3';
var state = b.HIGH; // Initial state
b.pinMode(LED, b.OUTPUT);
setInterval(flash, 250); // Change state every 250 ms
function flash() {
b.digitalWrite(LED, state);
if(state === b.HIGH) {
state = b.LOW;
} else {
state = b.HIGH;
}
}
Blink PocketBeagle on-board USRx LED
Goal: Blink USR3 LED on PocketBeagle.
Overview: BoneScript is a Node.js library customized for the Beagle family and featuring familiar Arduino function calls. Here we will use it to blink an LED built into your PocketBeagle.
Do this in the Cloud9 IDE:
1. Navigate to TechLab/internalLED.js and double-click on it.
2. Click the Run button in the toolbar to execute the script in the active file window
3. You will see the run configuration window open with a Stop button. Click the Stop button to halt the program.
4. Try changing the LED or blink time, save the program and run again.
TIP: Click the green bug to disable the debugger and begin execution quicker.
internalLED.js
1.
2.
Active File Window
Run Configuration Window
3.
TIP

## Slide 5
Read a button
Goal: Sense the external world by reading a digital input.
Overview: Reading a switch attached to a GPIO (general purpose input/output) port is as
easy as configuring the port as an input and attaching an interrupt handler to it. Note the buttons are “active low”.
Do this in the Cloud9 IDE:
1. Navigate to TechLab/pushbutton.js and double-click on it.
2. Click the Run button in the toolbar to execute the script in the active file window
3. Press the “L” button on TechLab and check the output (Value=1 or Value=0) in the configuration window. Click the Stop button on the IDE to halt the program.
Challenge #1: Can you modify the program to read from the “R” button?
Challenge #2: Can you modify the program to toggle the USR3 LED?
Challenge #3: Can you modify the program to turn the USR3 LED on with the “L” button and off with the “R” button?

## Slide 6
#!/usr/bin/env node
var b = require('bonescript');
var button = "P2_33";
console.log('Hit ^C to stop');
b.pinMode(button, b.INPUT, 7, null, null, doAttach);
function doAttach(err, x) {
if(err) {
console.log('pinMode err = ' + err);
return;
}
b.attachInterrupt(button, true, b.CHANGE, printStatus);
}
function printStatus(err, x) {
if(err) {
console.log('attachInterrupt err = ' + err);
return;
}
if(x.attached) {
console.log("Interrupt handler attached");
return;
}
process.stdout.write('value = ' + x.value + ' \r');
}
Read a button
pushbutton.js

## Slide 7
Read an analog sensor
Goal: Sense the external world by reading a variable analog input
Overview: Reading a light sensor attached to an analog input pin.
Do this in the Cloud9 IDE:
1. Navigate to TechLab/analogIn.js and double-click on it. 2. Click the Run button in the toolbar to execute the script in the active file window
3. Cover the light sensor and check the output in the configuration window. Click the Stop button to halt the program.
Challenge #1: Can you change how often the light sensor is read? What happens and why?
Challenge #2: Can you activate the USR3 LED based upon a voltage threshold from the light sensor?
Challenge #3: (Advanced Coding Lab) Try using the I2C accelerometer input from /sys/bus/iio/devices/iio:device1/in_accel_x_raw. Hint: use b.readTextFile()

## Slide 8
Read an analog sensor
analogIn.js
#!/usr/bin/env node
var b = require('bonescript');
var pin = 'P1_19';
console.log('Hit ^C to stop');
doAnalogRead();
function printStatus(err, x) {
if(err) {console.log('Got error: ' + err); return;};
process.stdout.write(pin + ': ' + (x*100).toFixed(1) +
'%, ' + (1.8*x).toFixed(3) + 'V \r');
setTimeout(doAnalogRead, 100);
}
function doAnalogRead() {
b.analogRead(pin, printStatus);
}

## Slide 9
Fade an LED
Goal: Utilize a hardware pulse-width-modulator (PWM) to light an LED with variable brightness
Overview: Linux provides LED drivers that understand how to utilize PWM drivers, making use of PocketBeagle’s built-in PWM hardware. They are controlled with simple text files where you can set the brightness.
Do this in the Cloud9 IDE:
1. Navigate to TechLab/fadeLED.js and double-click on it.
2. Click the Run button in the toolbar to execute the script in the active file window
3. You will see the run configuration window open with a Stop button. Click the Stop button to halt the program.
Challenge #1: Try changing the fade interval, save the program and run again.
Challenge #2: Try using the light sensor input to set the LED brightness.
Challenge #3: (Advanced Coding Lab)
Try using the I2C accelerometer input for all 3 color LEDs..

## Slide 10
#!/usr/bin/env node
var b = require('bonescript');
var LED = '/sys/class/leds/techlab::blue/brightness';
var step = 10, // Step size
min = 0, // dimmest value
max = 255, // brightest value
brightness = min; // Current brightness;
doInterval();
function doInterval(err, x) {
if(err) {
console.log('err = ' + err);
return;
}
setInterval(fade, 20); // Step every 20 ms
}
function fade() {
b.writeTextFile(LED, brightness);
brightness += step;
if(brightness >= max || brightness <= min) {
step = -1 * step;
}
}
Fade an LED
fadeLED.js

## Slide 11
Using Node-RED to read and write files
Goal: Read light sensor data and output to green LED brightness
Overview: Node-RED is a flow-based development tool developed originally by IBM for wiring together hardware devices, APIs and online services as part of the Internet of Things. Node-RED provides a browser-based flow editor, which can be used to create JavaScript functions. Linux turns devices into virtual files, making Node-RED well suited to interacting with the physical world.
Do this:
1. Open Node-RED by pointing your browser to http://192.168.7.2:1880
2. Make sure the big “DEPLOY” button in the top right corner is greyed-out by clicking it. This makes sure any changes you’ve made have been started on your PocketBeagle. The program will run continuously.
3. Click the highlightable button to the left of the “ON”. Cover the light sensor to notice the brightness of the green LED adjust.
4. Try double-clicking on each node to see the parameters used for the demo.
5. Click the highlightable button to the left of the “OFF” to stop adjusting the brightness of the green LED.
6. Explore
Challenge #1: Try updating the blue LED rather than the green LED. Remember to click the “DEPLOY” button to save and run your changes.
Challenge #2: Try reading from the I2C accelerometer rather than the light sensor.
Challenge #3: Use a “gpio in” node to use the status of the “L” or “R” buttons to update the LED.

## Slide 12
cd /sys/class/leds
ls
echo 1 > techlab\:\:seg0/brightness
config-pin p1.33 pwm
echo 10 > techlab\:\:red/brightness
cd /sys/class/gpio
config-pin p1.29 gpio
cat gpio45/value gpio117/value
Explore the Linux command line
Goal: Learn to send several basic commands to the shell
Overview: The true power of Linux to automate many aspects of your life cannot be achieved without some utilization of the command line shell. The Cloud9 IDE makes it easy to access this directly from your web browser. Another great resource for learning is linuxcommand.org.
Do this in the Cloud9 IDE:
1. Click in the terminal window at the bottom half of the IDE. You can also open a new terminal by clicking the “+” in the window tabs and selecting “New Terminal”.
2. Try typing in the “commands to try”. Press <ENTER> after each command. Take note of how the prompt changes to show you the current active directory. Use the up and down arrows to cycle through commands you’ve typed before, in case you want to repeat any.
Challenge #1: Can you repeat the last command below that prints GPIO values and change the values?
Challenge #2: Using the “watch” command, can you monitor the I2C accelerometer status?
Challenge #3: Can you use the “config-pin” command to switch the red LED to a GPIO, set it high and low and then switch it back to PWM mode? What happens if the red LED is in GPIO mode and you change the brightness with the “/sys/class/leds” entry?
commands to try
Some useful commands
pwd - show current directory
cd - change current directory
ls - list directory contents
chmod - change file permissions
chown - change file ownership
cp - copy files
mv - move files
rm - remove files
mkdir - make directory
rmdir - remove directory
cat - dump file contents
less - progressively dump file
vi - edit file (complex)
nano - edit file (simple)
head - trim dump to top
tail - trim dump to bottom
echo - print/dump value
env - dump environment variables
export - set environment variable
history - dump command history
grep - search dump for strings
man - get help on command
apropos - show list of man pages
find - search for files
tar - create/extract file archives
gzip - compress a file
gunzip - decompress a file
du - show disk usage
df - show disk free space
mount - mount disks
tee - write dump to file in parallel
hexdump - readable binary dumps

## Slide 13
Toggle LED based on a button press using a PRU
Goal: Utilize a programmable real-time unit (PRU) to read and set GPIOs.
Overview: A PRU is a microcontroller built into the PocketBeagle that can be programmed in C or assembly and controlled by the main ARM processor that runs Linux. Some pins can be directly mapped to PRU registered for the lowest possible latency, but other GPIOs can be utilized via the on-chip-peripheral (OCP) bus inside the processor. Here we’ll learn to execute an example written in C to access the direct-mapped PRU GPIOs.
Do this in the Cloud9 IDE:
1. Navigate to TechLab/led-button.pru0c and double-click on it.
2. Click the Run button in the toolbar to execute the script in the active file window.
3. Click the run configuration window and type ‘temppwd’ when prompted for the password.
Note: The program will keep running until you execute a different program or reboot.
4. Press the ‘R’ button to note the red RGB LED light up.
Challenge #1: The buzzer is on PRU0 output 3 (P2_30). Try setting its output at the same time as the LED.
Challenge #2: Try toggling the buzzer with a for loop when the button is pressed. You can use the ‘__delay_cycles’ function to add a delay. Each delay cycle should be 5ns, so 800Hz is 250000 cycles, a reasonable number to try.
Challenge #3: (Advanced Coding Lab)
Run TechLab/rgb.pru0c and note how the on-chip-peripherals are accessed as well as how a fade effect can be done easily creating a software pulse-width-modulator.

## Slide 14
#include <stdint.h>
#include <pru_cfg.h>
#include <pru_ctrl.h>
#include <stddef.h>
#include <rsc_types.h>
volatile register unsigned int __R30;
volatile register unsigned int __R31;
#pragma DATA_SECTION(init_pins, ".init_pins")
#pragma RETAIN(init_pins)
const char init_pins[] =
"/sys/devices/platform/ocp/ocp:P1_33_pinmux/state\0pruout\0" \
"/sys/devices/platform/ocp/ocp:P1_29_pinmux/state\0pruin\0" \
"\0\0";
void main(void) {
/* Invert GPIO input 7 to GPIO output 1 */
/* On TechLab, input 7 is the R button */
/* On TechLab, output 1 is the red in the RGB LED */
while(1) {
if(__R31 & (1<<7)) {
/* Clear output */
__R30 &= ~(1<<1);
} else {
/* Set outputs */
__R30 |= (1<<1);
}
}
}
struct my_resource_table {
struct resource_table base;
uint32_t offset[1];
};
#pragma DATA_SECTION(pru_remoteproc_ResourceTable, ".resource_table")
#pragma RETAIN(pru_remoteproc_ResourceTable)
struct my_resource_table pru_remoteproc_ResourceTable = {
1, /* we're the first version that implements this */
0, /* number of entries in the table */
0, 0, /* reserved, must be zero */
0, /* offset[0] */
};
Fade LEDs using a PRU
led-button.pru0c